## Slide 1: Ebode Camera Security Analysis
DXD946, MXY995, RXF964, HXX953, YXL1178

## Slide 2: Initial research
Reading packaging and manuals
Connected via ethernet
Possible server setup
Firmware Structure
Firmware Reverse Engineering
Web Connection
Network Analysis
Common Vulnerabilities

## Slide 3: Basic Information
Hardware
  MAC ID：54CDEE003896
  DDNS：http://g2339.oipcam.com (expired)
  Default username/password: admin/<empty>

## Slide 4: Setup
Setting a bridge between Wireless network and Ethernet network
Intercepting HTTP traffic

## Slide 5: Google hacking
Product information gathering
CVE history search (All exploits failed)
CGI documentation information(Useful)
http://www.foscam.eu/index.php/productattachments/index/download?id=129
Firmware download link

## Slide 6: Firmware structure
ROMFS
Compressed Linux.bin (ZIP)

## Slide 7: Firmware Reverse engineering
CGI List (Thanks to CGI document. We can know what they are doing easily)

## Slide 8: Firmware reverse engineering
Fake CGI…(Actually it only compare strings)

## Slide 9: Firmware reverse enginnering
Formatting code by IDE(Clion)
Check it one by one until 4th function. An arbitrary file including vulnerability was found.

## Slide 10: Arbitrary File read
Downloading file from this link without need any authentication
Admin account and Password is plaintext in memory
http://100.84.124.155/decoder_control.cgi?command=1&next_url=/proc/kcore

## Slide 11: APP connection
Official App is behind paywall
All open source apps tried didn't seem to work, some reasons:
  The Firmware and/or software may out-of-date
  App may have been fixed by an update
After the vulnerabilities found earlier, large possibility of vulnerabilities

## Slide 12: WEb connection
IP Camera Network analysis:
  Traffic sent from/to port 80 => (HTTP/1.1)
  Authorization method => (Basic)
    Credentials are exposed.
  Intercepting live stream and images.

## Slide 13: WEb connection
IP Camera Network analysis:
  Intercepting live stream and images.
    Export the packet
    Save .jpeg extension file
Sample picture of my flat ceiling

## Slide 14: Attack Mitigations
To ensure the ip camera network secure:
  Use HTTPS
  TLS/SSL Protocols
  Improved authentication
  Strong passwords

## Slide 15: Common vulnerabilities
Cross-Site Request Forgery
DNS Hijacking
Missing Function Level Access Control
X-FRAME-OPTIONS Missing (Click Hijacking)
No HTTPS
Arbitrary file read